Pealkiri
Disk management
Operating systems I800
Edmund Laugasson
edmund.laugasson@itcollege.ee
There has been used materials from Margus Ernits, Katrin Loodus when creating current slides.
Current document copying, distributing and/or modifying has been set out by one of the following licences by user’s choice:
* GNU Free Documentation Licence version 1.2 or newer
* Creative Commonsi Attribution + ShareAlike licence 4.0 (CC BY-SA)

---
Operating system external memory
- hard disks
- disk arrays
- Interchangeable discs
  - CD, DVD, BD etc
  - etc
- Flash and other memory devices

---
Disk structure
about SSD
how it works
video1
video2
- track
- cylinder
- sector
- head
- CHS (cylinder, head, sector)
- LBA Logical Block Addressing
  - every block has its own address
  - LBA address =c*H*S+h*S+(s-1)
    - c – cylinder, H – heads per cylinder, S – sectors per track, s - sector
- how rotating HDD works (videos)
  - https://en.wikipedia.org/wiki/File:Harddrive-engineerguy.ogv
  - https://en.wikipedia.org/wiki/File:HardDisk1.ogg

---
HDD (Hard Disk Drive) parameters
- Volume
  - 1 GB (GigaByte) (10^9) and 1 GiB (GibiByte) (2^30)
  - HDD manufacturers are using GB = 1000 MB
  - technically they are correct
- the quantity of tracks, cylinders, heads and sector size
- speed
  - rotating speed
    - revolutions per minute (rpm)
    - 5400, 7200, 10000, 15000
http://www.storagereview.com/ssd_vs_hdd

---
HDD parameters 2
- speed (continues)
  - read, write speed
    - random block reading (important seek time)
    - linear reading (important fast rotating speed)
  - seek time – time spent to find exact block
  - access time – time spent to access certain block
  - latency – „wasted time“
- Reliability
  - MTBF mean time between failures (in hours)
    average working time without failures
  - S.M.A.R.T. Self-Monitoring, Analysis and Reporting Technology
    https://help.ubuntu.com/community/Smartmontools
    https://en.wikipedia.org/wiki/Lm_sensors - Linux-monitoring sensors

---
Naming disks in system
- UNIX-like and Linux
  - SCSI, SATA, SAS /dev/sd*
    - first SCSI disk /dev/sda
    - second SCSI disk /dev/sdb
  - IDE /dev/hd*
    - first IDE master disk /dev/hda
    - second IDE slave disk /dev/hdb
    - third IDE master disk /dev/hdc
- MS Windows
  - A:, B:, C:, D: etc disks
- Mac
  - /dev/disk0s1

---
Naming disks in system 2
- to avoid confusion there are alternative naming options
  - /dev/sd*
  - UUID = 5f473d92-42fd-459f-8bbc-3e52cbf1d368
    - GRUB (/boot/grub/grub.cfg), /etc/fstab are using
      (NB! Ensure which file can be changed manually!)
    - blkid (block devices ID’s)
    - lsblk (list block devices)
  - give names for partitions like LABEL = backup

---
Naming disks in Linux
- ls -l /dev/sda
  - brw-rw---- 1 root disk 8, 0 2008-02-24 03:26 /dev/sda
  - access rights: owner (root), group (disk)
  - device class number (major device no) 8 (SCSI devices)
  - device number (minor device no) 0 (first device)
- /dev/sda first SCSI disk
- /dev/sdb second SCSI disk
- /dev/hda first channel master disk
- /dev/hdb first channel slave disk
- /dev/hdc second channel master disk
- http://tldp.org/HOWTO/Partition/devices.html

---
Naming disks in Linux 2
- device classes
  - important to read for driver developers (see also http://www.linux-drivers.org/, https://www.kernel.org/doc/)
  - Linux Assigned Names and Numbers Authority (LANANA),
    Linux Device List
  - https://en.wikipedia.org/wiki/Linux_Assigned_Names_and_Numbers_Authority
  - http://www.lanana.org/docs/device-list/ (search: 8 block)
  - https://www.kernel.org/pub/linux/docs/lanana/device-list/
- devices – in UNIX-like (incl Linuxis) device is a file, https://en.wikipedia.org/wiki/Device_file
  - c character device unbuffered direct access to hardware
    (in Linux a virtual device generally)
  - b block device buffered access to hardware
    (in Linux a physical device generally)
  - http://stackoverflow.com/questions/1823743/knowing-a-device-special-file-major-and-minor-numbers-in-linux

---
Partitions
- disk can be splitted into partitions
- partition table goes into 0-sector, MBR (Master Boot Record)
  - up to 446 B boot loader (e.g. GNU GRUB)
  - 512 B together with partition table
  - cylinder 0, track 0, sector 0
  - EST https://wiki.itcollege.ee/index.php/MBR
  - ENG https://en.wikipedia.org/wiki/Master_boot_record
- Nowadays GPT (EFI), where partition table is directly written onto partition and not in separate, special place
  - with Intel Itanium processor machines
  - no quantity limit, size >2TB allowed
  - EST https://wiki.itcollege.ee/index.php/GPT
  - ENG https://en.wikipedia.org/wiki/GUID_Partition_Table

---
Partitions 2
- there was a belief that 4 partitions would be enough
  - primary partition, up to 4 (MBR, also DOS partition table)
    - disk names between 1-4 (/dev/sda1...sda4)
  - extended partition,
    one extended partition per disk is allowed
    - disk names between 1-3 (/dev/sda1...sda3)
    - extended partition with at least one logical volume
      - disk names between 5 - * (/dev/sda5...sda*)
    - lsblk (to view, man lsblk), http://linux.die.net/man/8/lsblk
    - df -h (free disks space, man df), https://linux.die.net/man/1/df

---
Partitions in MS Windows
- Understanding Disk Partitions
  https://technet.microsoft.com/en-us/library/dd799232(v=ws.10).aspx
- MS Windows and GPT FAQ
- https://msdn.microsoft.com/en-us/library/windows/hardware/dn640535(v=vs.85).aspx
- EST https://wiki.itcollege.ee/index.php/DISKPART
- ENG https://technet.microsoft.com/en-us/library/cc770877(v=ws.11).aspx
by default based on MS Windows 7 and MS Windows Server 2008 R2 GPT disk partitioning table:
MSR -Microsoft® Reserved Partition

---
creating partitions
- disk information
  - fdisk -l [disk] e.g.: fdisk -l /dev/sda
  - Disk /dev/sda: 80.0 GB, 80026361856 bytes
  - 255 heads, 63 sectors/track, 9729 cylinders
  - Units = silindrit of 16065 * 512 = 8225280 bytes
  - Disk identifier: 0xc51bc51b
  - Device Boot Start End Blocks Id System
  - /dev/sda1 * 1 5571 44749026 7 HPFS/NTFS
  - /dev/sda2 5572 9552 31977382+ 83 Linux
- tools to create partitions
  - fdisk
  - cfdisk
  - parted (suggested to use in case of GPT partition table)
  - https://en.wikipedia.org/wiki/List_of_disk_partitioning_software

---
using fdisk
- fdisk /dev/sd*
- m manual
- p displays partition table (print)
- n creates a new partition (new)
- d deletes a partition (delete)
- q will quit without saving partition table (quit)
- w writes partition table onto HDD (write)

---
creating a file system
- before you can use the partition, a file system must be created
  - ENG https://en.wikipedia.org/wiki/File_system
  - EST https://wiki.itcollege.ee/index.php/Failisüsteem
- NB! Please pay attention to symbols how to mark disks compared with fdisk
- mkfs -t type partition
  - mkfs -t ext4 /dev/sdb*
  - mkfs.ext4 /dev/sdb*

---
mounting partitions
- the mount command is used
- mount -t <type> <parameters> <device> <full directory path as a mount point>
  - mount -t ext4 -o rw /dev/sda2 /home
    - will mount first SCSI device under the directory /home
  - mount -t ntfs /dev/sda1 /mnt/ntfs
    - will mount in read-only mode NTFS partition sda1 under the directory /mnt/ntfs
  - ntfs-3g – 3rd generation NTFS driver for reading and writing
    - mount -t ntfs-3g /dev/sda1 /mnt/ntfs/
    - ntfs-3g /dev/sda1 /mnt/ntfs
- unmount
  - umount /home
- ENG
  - man mount, man ntfs-3g, etc
- EST
  - https://wiki.itcollege.ee/index.php/Mount
  - https://wiki.itcollege.ee/index.php/NTFS_vs_Ext4
  - https://wiki.itcollege.ee/index.php/NTFS_failis%C3%BCsteemi_kasutamine_linuxis_v%C3%B5i_macis

---
mount partitions at boot: /etc/fstab
- man fstab, EST https://wiki.itcollege.ee/index.php/Fstab
- https://guidgenerator.com/ - UUID (GUID)
$ cat /etc/fstab
# /etc/fstab: static file system information.
#
# Use 'blkid' to print the universally unique identifier for a
# device; this may be used with UUID= as a more robust way to name devices
# that works even if disks are added and removed. See fstab(5).
#
# <file system> <mount point> <type> <options> <dump> <pass>
# / was on /dev/sda5 during installation
UUID=da17263a-2afb-42c9-86fb-abe4f55c12f4 / ext4 errors=remount-ro,noatime,commit=600 0 1
# /home was on /dev/sdb1 during installation
UUID=ba77de4a-0a35-4968-bf97-d93840165904 /home ext4 defaults,noatime,commit=600 0 2
# swap was on /dev/sda1 during installation
#UUID=68682f78-7849-46c5-a2fa-125f3ee72e99 none swap sw 0 0
/dev/mapper/cryptswap1 none swap sw 0 0
#/dev/disk/by-uuid/7fa84b49-ae7c-4a64-be4e-04c22a32ade0 /mnt/7fa84b49-ae7c-4a64-be4e-04c22a32ade0 auto nosuid,nodev,nofail,x-gvfs-show,errors=remount-ro,noatime,commit=600 0 0
/dev/disk/by-uuid/6cfbe92f-78f7-4eb9-ab17-fe09267a1bb5 /mnt/data2 auto nosuid,nodev,nofail,noauto,errors=remount-ro,noatime,commit=600 0 0
MS Windows’is UUID:
https://msdn.microsoft.com/en-us/library/windows/desktop/aa373928(v=vs.85).aspx

---
/etc/fstab
- UUID=6...703e / ext4 defaults,acl,errors=remount-ro 0 1
- device
  - can be as /dev/sda1
  - can be as UUID=
  - can be as LABEL=
- mount point
  - where the device will be mounted
    - e.g. / root directory
    - e.g. /home for user home directories (useful as there is no need to backup user data when new system installation needed)

---
/etc/fstab (2)
- UUID=6...703e / ext4 defaults,acl,errors=remount-ro 0 1
- file system type
  - e.g. ext3, ext4, reiserfs, btrfs, ntfs, cifs etc
- Options
  - sync/async – synchronous or asynchronous I/O
  - noauto – file system will be not mounted during boot

---
/etc/fstab (3)
- UUID=6...703e / ext4 defaults,acl,errors=remount-ro 0 1
- noexec – running binary executables prohibited
- suid – suid bit allowed
- ro – will be mounted as read-only
- user – user can mount the file system
- defaults – default settings will be used (differs by file system)
  - rw, suid, dev, exec, auto, nouser, async
- acl – the Access Control List will be allowed

---
File system check
- File systems may be broken sometimes
  - e.g. pull out a memory stick without syncing in first place
    - use sync command in CLI
  - current passes away
- fsck [parameters] -t <type> <device>
- also fsck.* commands can be used
  - fsck.ext4 -p /dev/sda1

---
Restore partitions
- gpart /dev/sdX
  - takes time but guesses partitions and displays the table
  - not installed by default
- gpart -W /dev/sdX /dev/sdX
  - when table seems to be logical then it will be written onto disk
- it would be a good idea to make a backup from your partition table and keep it in safe and secure place
  - dd if=/dev/sda of=sda.mbr count=1 bs=512
  - sfdisk -d /dev/sda > sda.tabel
- to restore:
  - dd if=sda.mbr of=/dev/sda
  - sfdisk /dev/sda < sda.tabel

---
Swapping
- Swap area is used to extend RAM on HDD
- makes RAM usage more flexible
- virtual address space
  - physical aadress
  - MMU memory management unit - will translate virtual memory address into physical
  - virtual address
  - memory page
- swapping
  - swap in/swap out

---
SWAP (2)
- when any of memory part is not used then corresponding memory blocks are written to swap area
- swap can be separate partition or file on the partition
  - MS Windows: would be good idea to put onto separate partition
- create: mkswap /dev/sdb1
- activate: swapon /dev/sdb1
- allow on boot in file /etc/fstab
  - /dev/sdb1 none swap sw 0 0
  - UUID=<hash> none swap sw 0 0

---
SWAP (3)
- creating a swap file
  - dd if=/dev/zero of=/swapfile bs=1024 count=1048576
  - will create a 1GiB file with zeros inside
  - create: mkswap /swapfile
  - activate: swapon /swapfile

---
SWAP (4)
- swap size
  - in old times there was a thumb rule 1-2 times of RAM size
  - nowadays can be less
  - on wearable computers it would be useful to create ⩾RAM size as hibernate will use swap area (in case of Linux)
  - in case of SSD disk the swap area:
    - ensure that TRIM works
      - https://askubuntu.com/questions/464306/a-command-which-checks-that-trim-is-working
    - there is suggested to avoid hibernate
    - using RAM-drive and avoiding swap area, -file
    - SSD
      - ENG https://en.wikipedia.org/wiki/Solid-state_drive
      - EST https://wiki.itcollege.ee/index.php/SSD_kettad
    - https://en.wikipedia.org/wiki/RAM_drive
    - https://en.wikipedia.org/wiki/List_of_RAM_drive_software

---
Problem
- using disks, several issues will rise
  - perfomance – increasing disk speed and size is not unlimited. Fast disks are expensive
  - Latency – disks with small latency are expensive
  - Reliability – hard disks have MTBF (mean time between failures). Quite often the disk will failure in first place.
  - Planning disk space is quite challenging – sometimes is needed more, sometimes less

---
Problem solving
- Pefomance
  - write and read in parallel from multiple disks
- Latency
  - read and write in parallel from multiple disks
- Reliability
  - create redundancy and duplicate data on multiple disks
- Planning and partitioning
  - use the system that allows change partition size

---
RAID
- RAID Redundant Arrays of Independent Disks
- Redundancy is used to increase reliability and perfomance
- Mean Time Between Failures (MTBF)
  - measured in hours
- ENG https://en.wikipedia.org/wiki/RAID , https://en.wikipedia.org/wiki/Category:RAID
- EST https://wiki.itcollege.ee/index.php/RAID
- EST https://wiki.itcollege.ee/index.php/Raid_kettas%C3%BCsteemid
- EST https://et.wikipedia.org/wiki/S%C3%B5ltumatute_ketaste_liiasmassiiv
- ENG https://en.wikipedia.org/wiki/Mean_time_between_failures

---
RAID
- Stripe data storage – data blocks are stored across over multiple disks
- Redundancy – data is duplicated on multiple disks
  - disk mirroring
- Error Correction Code – there will be checksums calculated that can be used to discover errors and in some cases also fix
- Rebuild – restore disk based on information at other disks
- Spare disk – a backup disk connected to the system

---
RAID 0
- RAID 0
  - data stored as striped on multiple disks
  - increases read - and write speed
  - reliability does not increase but reduce
  - Min disks: 2. Data storage volume is a sum of disks
block 2
block 3
block 1
block 2
block 3
block 4
block 1
block 4

---
RAID 1
- RAID 1
  - disks mirroring or creating a redundancy
  - reliability will be increased because data is duplicated
  - reading speed will be increased as data can be read from multiple disks at the same time
  - writing speed is the same as data will be written onto multiple disks
  - Min 2 disks. Volume = disks volume/2
block 1
block 2
block 3
block 4
block 1
block 1
block 2
block 2

---
RAID 5
- RAID 5
  - stripe storage disks
  - shared parity check (parity information is shared between disks)
  - damaged disk data will be restored due to parity information on other disks
  - creating parity information takes a time
large reading speed
average writing speed
slow array restore
file -, mail -, media server
most widely used
block 2
block 1
parity
block 1.3
block 1
block 2.1
block 1.1
block 2.2
block 1.2
block 2
parity

---
RAID 1+0
- RAID 1+0
  - multiple mirrors in stripe storage
  - combines RAID0 and RAID1 good characteristics (redundancy and speed)
  - used in case of database servers and other high perfomance apps
  - high price
block 2
block 1.2
block 2.1
block 1.1
block 2.1
block 1.1
block 2.2
block 1.2
block 2.2
RAID0
RAID1
RAID1
block 1
=
=

---
rich world of RAID
- Nested RAID:
  - RAID0+1
  - RAID5+0
  - RAID6+0+0 jne
- intermediate levels
  - RAID2, stripe storage on bit level
  - RAID3, stripe storage on byte level
  - RAID4, stripe storage on block level (parity information on separate disk)
  - http://www.acnc.com/raid

---
RAID controller
- manages I/O queries
- restores data from spare drives when needed
- monitor errors
- hardware and software RAID-controller
- ENG https://en.wikipedia.org/wiki/Disk_array_controller
- EST https://wiki.itcollege.ee/index.php/RAID_controller
- ENG http://www.tldp.org/HOWTO/Software-RAID-HOWTO.html
- EST https://wiki.itcollege.ee/index.php/Softi_RAID_Ubuntu_baasil.
- ENG https://help.ubuntu.com/community/Installation/SoftwareRAID
- EST https://wiki.itcollege.ee/index.php/Tarkvaraline_RAID_Ubuntus

---
RAID summary
  - increases reliability and/or speed
  - is more expensive than regular storage
  - will increase complexity that may cause problems
  - Will not replace the need to do backup
  - allows renew system to breake mirroring so the one disk will keep original system
    - when there is a success of renewing the system then new system will be mirrored to another disk after rebuilding RAID
    - when renewing system caused problems then data will be mirrored back from old drive

---
LVM
- Logical Volume Manager
- created as logical layer between disks and sile system
  - flexible way to configure physical disks
  - widely used in large amount of disks deployments
Disks
RAID
LVM
File system

---
LVM
- allows
  - add new disks to the system by enlarging existing file system (e.g. adding additional storage space for home folders)
  - remove old disks from the system
    - data can be easily copied to new disks and unmount old ones
  - Snapshot copy
  - can be combined with RAID usage

---
LVM
- block device
  - hard disks or partitions
- disk groups or volume groups
- logical disks
volume group
logical disk
disk 2
disk 1

---
LVM usage steps
- pv* - physical volume commands
- vg* - volume group commands
- lv* - logical volume commands
- initialize disks
- create a volume group and bind disks with that
- share logical disks (partitions)
- format logical disk with file system
- mount formatted logical disk

---
LVM
- to use LVM there should be disk or partition prepared as a physical volume (all commands as root user)
  - pvcreate <disk1> <disk2> ...
  - e.g. pvcreate /dev/sdb1
- created physical volumes can be viewed:
  - pvdisplay

---
LVM
- after preparing (marking) disks there should be created a volume group
  - vgcrearte <group> <disk1> <disk2> ...
  - e.g.: vgcreate mysql /dev/sdb1
  - here has been created a volume group named mysql by including device /dev/sdb1 (in group there can be 1....n partitions)
- created volume groups can be displayed:
  - vgdisplay

---
LVM
- vgrename <oldgroup> <newgroup>
  - e.g.: vgrename mysql db
- creating new logical volume using lvcreate
- lvcreate -L 100G -n lv01 mysql
  - Logical volume "lv01" created
- after creating logical volume there can be created a file system on that and mounted under certain directory and start using it
- mkreiserfs /dev/vg1/lv01
- will create a reiserfs file system on logical volume lv01

---
LVM
- extending: lvextend
  - lvextend -L150G /dev/mysql/lv01
- reducing lvreduce
  - lvreduce -L1G /dev/mysql/lv01
- removing physical disk from LVM array
  - pvremove <disk1> <disk2> ...
  - e.g.: pvremove /dev/sdb1 /dev/sdc1 /dev/sdd1 /dev/sde1
- there can be removed 1...n partitions

---
Disk quota
- sometimes you need to limit storage space given for users
- there will be used a disk quota for that
- sudo apt-get install quota
- when mounting, please use appropriate quota parameter
  - mount -o quota /dev/sdb2 /home
- for automatic mounting through /etc/fstab please use usrquota and/or grpquota parameter
  - /dev/sda2 /home ext4 defaults,usrquota 1 2

---
Disk quota
- to monitor disk quota limits
  - quotacheck -avug
- this would be useful to watch periodically after certain amount of time
- setting up quota for user and group
  - edquota -u student
  - edquota -g students
- soft limit – can be exceed temporarily
- hard limit – cannot be exceeded (data writing denied when reaching the limit)

---
Storage Area Network (SAN)
ENG https://en.wikipedia.org/wiki/Storage_area_network
EST https://wiki.itcollege.ee/index.php/SAN
user
storage
Servers are using SAN network
to access storage resources
user can access to
 network services
IP router
SAN switch/router

---
Network Attached Storage (NAS)
ENG https://en.wikipedia.org/wiki/Network-attached_storage
EST https://wiki.itcollege.ee/index.php/NAS
user
disks
Server can use
local disk
IP router
SAN switch/ruuter
File level access
Server can use
SAN-based solution
NFS
CIFS/SMB
FTP, SSH

---
Links
- https://help.ubuntu.com/community/PartitioningSchemes
- EST https://wiki.itcollege.ee/index.php/Partitsioonid
- EST https://wiki.itcollege.ee/index.php/Kettajaod
- http://manpages.ubuntu.com/manpages/xenial/man8/gdisk.8.html
- EST https://wiki.itcollege.ee/index.php/Gdisk
- https://en.wikipedia.org/wiki/Disk_partitioning
- https://en.wikipedia.org/wiki/Partition_type
- https://support.microsoft.com/en-us/kb/302873 - GUID FAQ, MS Windows

---
Links
- RAID WikiPedia http://en.wikipedia.org/wiki/RAID
- RAID flash demo
  http://www.acnc.com/raid.html
- SAN in Linux
  http://www.linuxjournal.com/magazine/use-linux-san-provider
  http://iscsitarget.sourceforge.net/
  https://wiki.itcollege.ee/index.php/ISCSI_target_ja_initiator
  http://www.openfiler.com/, vt ka alternatiive
- NAS solutions:
  - OpenMediaVault
    https://www.howtoforge.com/tutorial/install-open-media-vault-nas/
  - FreeNAS
    https://www.howtoforge.com/network_attached_storage_with_freenas

---
Links (LVM)
- LVM for beginners http://www.howtoforge.com/linux_lvm
- http://www.tldp.org/HOWTO/LVM-HOWTO/
- http://www.debian-administration.org/articles/410
- http://linuxdevcenter.com/pub/a/linux/2006/04/27/managing-disk-space-with-lvm.html?page=1
- http://docs.redhat.com/docs/en-US/Red_Hat_Enterprise_Linux/4/html/Cluster_Logical_Volume_Manager/

---
Links (RAID)
- Software RAID in Ubuntu https://help.ubuntu.com/community/Installation/SoftwareRAID
  https://wiki.ubuntu.com/Raid
- FakeRAID - https://help.ubuntu.com/community/FakeRaidHowto
- RAID in server https://help.ubuntu.com/lts/serverguide/advanced-installation.html
- RAID in Linux https://raid.wiki.kernel.org/index.php/RAID_setup
- RAID intro http://www.linux-mag.com/id/7924/
- Gnome Disks
  https://en.wikipedia.org/wiki/GNOME_Disks
  http://askubuntu.com/questions/500549/how-to-run-gnome-disk-utility
- http://www.tldp.org/HOWTO/Software-RAID-0.4x-HOWTO-2.html
- http://www.raid-calculator.com

---
Questions?

---
Thank you for your attention!